SAFU
SAFU PDU Types
(01h) CONNECT → (PSTRING root, caps)
(02h) CONNECTED ← (caps, OBJREF[] root)
(03h) INVOKE → (OBJREF, PSTRING, any[])
(04h) RESULT ← (any[])
(05h) INVOKEASYNC → (OBJREF, token, PSTRING, any[])
(06h) RESULTASYNC ← (token, any[])
(07h) POLL →
(08h) EVENT ← (OBJREF, PSTRING, any[])
(09h) SUBSCRIBE → (OBJREF, PSTRING)
(0Ah) UNSUBSCRIBE → (OBJREF, PSTRING)
(0Bh) DELETED ← (OBJREF)
(0Ch) CALLBACK ← (DELEGATE, any[])
(10h) P2P_EXPOSE (OBJ)
(11h) P2P_UNEXPOSE (OBJ)
(12h) P2P_REQUEST (OBJ, OBJ, token, PSTRING, any[])
(13h) P2P_RESPONSE (OBJ, OBJ, token, PSTRING, any[])
(14h) P2P_EVENT (OBJ, OBJ, token, PSTRING, any[])
(FFh) FRAME ERROR

PDU Delivery:
Use TPKT (RFC 1006) over TCP or TLS/TCP. The traffic is half-duplex unless the client negotiates full duplex capabilities.
Subscription is not required to fire an event.

Basic SAFU types (on the wire)
Number (in network byte order)
PSTRING: 16-bit length (bytes for ASCII incl. UTF-8, pairs for UTF-16), followed by actual string, no termination.
OBJREF: 32-bit integer. They are valid for the connection only. 0 is for the global object.
Token: the same, but no “object” semantics.
Delegate: 64-bit value, assigned by the client.
Any: 1 byte type specifier, actual data (if applicable). Defined types are:
0xh – 32-bit integer types. 00 – unsigned, 01 – OBJREF, 02 – HRESULT.
1xh – other integer types. 1h – unsigned (flag); 12h – 1 byte, 14h – 2 bytes, 16h – 8+ bytes.
2xh – PSTRING. 28h=UTF-16, 20h=UTF-8 (or ASCII, or Extended ASCII). 3 least significant bits define semantics: 0 – plain string, 1 – URI, 2 – HTML or HTML 6.0 or HTML 6A, 3 – MIME type, 4 – date/time (ISO format), 5 – URL encoded, 6, 7 – reserved.
30h – vector (1D array); followed by base type (1 byte) and length (count of items – 2 bytes), then actual data.
31h – tuple; followed by 32-bit size (in bytes), then actual data (of any). May be nested.
32h – delegate.
40h – decimal (BCD) <integral part digits, fractional part digits>
50h-57h – rectangular array (3 bits for no. of dimensions -2, base type (1 byte), length (2 bytes) of each dimension, actual data).
58h – reserved for a triangular array (not used; tuple+vector combination instead)
6xh – floating point (60h – single, 61h – double, 62h – extended, 63h – Pascal real 6 bytes).
FDh – Any (reserved).
FEh – DBNull, a special constant. No data.
FFh – Empty (no value). No data.
OBJ: 1 byte length followed by actual reference.